## Slide 1: Outline
Pulse Width Modulation
Oscilloskop projekt
  Delelementer
  Signalgenerator
  Analyse af et digital system (SigGenDatapath)
  Sinus Look-up table
  Block RAM/ROM
  Xilinx Core Generator

## Slide 2: Digital vs. Analogue signals
High
0V
3.3V
Low
A signal from a digital system is in principle an analogue signal
Placing a low pass filter in front of a digital signal will average out the digital pulses
Digital system
VDig
VDig
VAna
VAna

## Slide 3: Puls Width Modulation
Pulse Width Modulation (PWM) is an technique to control the amplitude of a signal (after filtering) by switching on-off the source
The time spend in on-state as compared to the off-state determines the filtered amplitude. This is also called Duty-Cycle
Digital PWM is normally done by a repetitive process
High (on)
0V
3.3V
Low (off)
T: PWM Period is the time duration of one PWM cycle.
t: Pulse With is the time spend in on-state during one PWM Period
D: Duty-cycle is the relative time spend in on-state (t/T)
The analogue level (after filtering) is determined by the duty-cycle
VAna = 3.3V * Duty-cycle
T
Repetition
t
PWMout

## Slide 4: Digital Puls Width Modulation
High (on)
0V
3.3V
Low (off)
T
t
PWM Resolution is the minimum change that can be made to the duty-cycle
Consider the PWM period being accomplished by a 8-bit counter (PWMcnt 0 – 255).
The PWM period start at 0 (zero) and end at 255 and a new PWM period then start.
The on-period can only be adjusted in quantum of one PWMcnt count
PWMcnt
0
1
2
3
4
5
6
7
255
254
252
253
254
255
0
1
The PWM resolution would then be:
Normally the PWM resolution is just referred to as ”8-bit” resolution
0
1
2
3
PWMout

## Slide 5: Digital to Analog Converter
Based on the PWM principle
Reset
Clk
PWMcnt
8
SigAmpl
8
-
+
Reset
Comparator
PWMout
Digital
PWMmodule
PWMcount
PWMcompt
Q
Analogue
VAna
C
R

## Slide 6: Øvelse D6
Pulse Width Modulation

## Slide 7: Øvelse
BTN3
BTN3
MClk
Clk
SW
8
ClkDiv
LYSregul
U1
R
TimeP
4
50MHz
PWMmodule
U2
SigAmpl
Rst
Reset
PWMout
LD
Bestem styrken af lysdioden ved hjælp af skyde knapperne

## Slide 8: Oscilloskop Projekt
I 3-ugers perioden skal I lave et system der består af en signalgenerator og et oscilloskop som styres fra en brugerflade på en PC. Systemet er baseret på Spartan-3 FPGA bordet og Z8-Encore MCU bordet som I har arbejdet med i 13-ugersperioden. Systemets elementer kan ses af nedenstående diagram:

## Slide 9: Systemets delelementer
Systemets elementer kan ses af nedenstående diagram:
Analog spænding
ADC
UART
Måle-data til PC
Opsætning fra PC
SPI
Frekvens
Amplitude
Shape

## Slide 10: Signalgenerator
Signalgeneratoren er baseret på et signalbehandlingsprincip der kaldes Pulse Width Modulation (PWM). Tanken bag PWM er at middelværdien (lavpasfiltreret) af et digitalt signal har en analog spænding (0V – 3.3V). Ved at pulse den digitale udgang (PWMOut) på passende vis kan man således generere en analog spænding. Denne spænding kan så være konstant eller periodisk varierende (enten som firkantet, savtakket eller sinusformet). Der er til projektet lavet en VHDL kode som kan bruges som udgangspunkt for signalgeneratoren.
BTN0
BTN1
BTN2
SW
BTN3
CLK
AN
CAT
PWMout
LD

## Slide 11: Udleveret Signalgenerator

## Slide 12: Pause

## Slide 13: SigGenDatapath
VHDL code for the entity of the SigGenDatapath component
library IEEE; use IEEE.STD_LOGIC_1164.ALL; use IEEE.STD_LOGIC_ARITH.ALL; use IEEE.STD_LOGIC_UNSIGNED.ALL; entity SigGenDatapath is generic( PWMinc : std_logic_vector(6 downto 0) := "0010000" ); Port ( Reset : in std_logic; Clk : in std_logic; SigEN : in std_logic; Shape : in std_logic_vector(1 downto 0); Ampl : in std_logic_vector(7 downto 0); Freq : in std_logic_vector(7 downto 0); PWMOut : out std_logic); end SigGenDatapath; architecture Behavioral of SigGenDatapath is signal SigCnt, FreqInc: std_logic_vector(11 downto 0); signal Sig, SigSquare, SigSaw, SigSinus : std_logic_vector(7 downto 0); signal SigAmpl: std_logic_vector(6 downto 0); signal MulC: std_logic_vector(15 downto 0); signal PWMcnt: std_logic_vector(6 downto 0) := "0000000"; signal PWM, PWMwrap : std_logic; Begin See following 3 slides end Behavioral;
Reset
PWMout
SigGenDatapath
Clk
Shape
2
Ampl
8
Freq
8
SigEN
PWMinc
7
PWMinc is a generic input value that can be changed in the port map.
For HW implementation PWMinc should be 1.
For simulation it should be ”0010000” (default)

## Slide 14: PWM part of SigGenDatapath
VHDL code for the PWM part of SigGenDatapath
PWMcount: process(Reset, Clk) begin if Reset = '1' then PWMcnt <= "0000000"; elsif Clk'event and Clk = '1' then PWMcnt <= PWMcnt + PWMinc; end if; end process; PWMdec: PWMwrap <= '1' when PWMcnt = "0000000" else '0'; PWMcomp: PWM <= '1' when PWMcnt <= SigAmpl else '0'; PWMon: PWMout <= PWM when SigEn = '1' else '0';
PWMinc
7
Reset
Clk
PWMcnt
7
SigAmpl
7
-
+
7-bit counter
Comparator
PWMout
PWMCount
PWMDec
PWM
PWMon
PWMComp
PWMwrap
Inc
Q
Reset
SigEN

## Slide 15: Amplitude part of SigGenDatapath
VHDL code for the Amplitude part of SigGenDatapath
SigMux: Sig <= X"FF" when Shape = "00" else SigSquare when Shape = "01" else SigSaw when Shape = "10" else SigSinus; AmplDec: process(Ampl, Sig) variable MulC: std_logic_vector(15 downto 0); begin MulC := Sig * Ampl SigAmpl <= MulC(15 downto 9); end process;
SigAmpl
7
SigMux
AmplDec
Sig
8
X”FF”
8
SigSq uare
8
SigSaw
8
SigSinus
8
Ampl
8
Multiplier
00
01
10
11
Sel
Shape
2

## Slide 16: Signal part of SigGenDatapath
VHDL code for the signal part of SigGenDatapath
FreqEnc: FreqInc <= "00" & Freq(7 downto 6) & Freq(5 downto 4) & '0' & Freq(3 downto 2) & '0' & Freq(1 downto 0); SigCount: process (Reset, Clk) begin if Reset = '1' then SigCnt <= X"000"; elsif Clk'event and Clk = '1' then if PWMwrap = '1' then SigCnt <= SigCnt + FreqCnt; end if; end if; end process; SquareDec: SigSquare <= "00000000" when SigCnt < X"800" else "11111111"; SawDec: SigSaw <= SigCnt(11 downto 4); SinusDec : entity WORK.SinusLUT PORT MAP ( clka => Clk, addra => SigCnt, douta => SigSinus);
FreqEnc
FreqInc
12
Reset
Clk
Freq
8
SawDec
SigCnt
12
SigSaw
8
SquareDec
SigSquare
8
SinusDec
SigSinus
8
PWMwrap
SigCount
12-bit counter
Inc
Q
Reset
En
Clk
addra
douta
clka
ROM

## Slide 17: Sinus Signal Generation
SinusDec
SigSinus
8
Clk
addra
douta
clka
ROM
SigCnt
12
Look-up table:
Consider SinusDec as a bookcase with 212 = 4096 different shelfs
On each shelf is an 8-bit value
SigCnt points out the shelf
SigSinus is the 8-bit value pointed out
The memory needed for this block is
212 * 8bit = 32768 Flip-Flop registers
=========================================================================
* Final Report *
=========================================================================
Device utilization summary:
---------------------------
Selected Device : 3s200ft256-4
Number of Slices: 38 out of 1920 1%
Number of Slice Flip Flops: 29 out of 3840 0%
Number of 4 input LUTs: 70 out of 3840 1%
Number of bonded IOBs: 41 out of 173 23%
Number of MULT18X18s: 1 out of 12 8%
Number of GCLKs: 1 out of 8 12%
From Sequential SquareSum example

## Slide 18: Block RAM/ROM
From: Using Block RAM in Spartan-3 Generation FPGAs
Xilinx Core Generator
Use the Xilins Core Generator to instantiate Block ROM for the SinusLUT component
221184
Block RAM in the Spartan FPGA can be used as ROM for the Sinus look-up table

## Slide 19: Implementing SinusLUT (1)

## Slide 20: Implementing SinusLUT (2)
Single Port ROM
Read Width: 8 (bit)
Read Depth: 4096

## Slide 21: Implementing SinusLUT (3)
******************************************************************
******** Example of Single Port Block Memory .COE file *********
******************************************************************
; Sample memory initialization file for Single Port Block Memory,
; v3.0 or later.
;
; This .COE file specifies initialization values for a block
; memory of depth=16, and width=8. In this case, values are
; specified in hexadecimal format.
memory_initialization_radix=16;
memory_initialization_vector=
ff,
ab,
f0,
11;
Sinus.COE

## Slide 22: Implementing SinusLUT (3)
=(1+SIN(2*PI()*A1/4096))*127
=DEC2HEX(B1)&","
Use Excel to make the sinus look-up table in the COE format

## Slide 23: Implementing SinusLUT (4)